## Slide 1: CS Robotics Seminar F16 (Week 1) – Sept. 19, 2016 “Shape Based Compliance in Locomotion” M. Travers, J. Whitman, P. Schiebel, D. Goldman, H. Choset Robotics Science and Systems (RSS) 2016
Presented By: Colin Rennie

## Slide 2
Videos

## Slide 3
Videos

## Slide 4
Background: Admittance Control and Compliance
Shape-Based Compliant Control
Whole Body Shape-Based Compliance (Snake)
Decentralized Shape Modulation
Outline

## Slide 5
Admittance Control
  Control approach which is the inverse of impedance control
  Defines motions as a function of external force input
Background: Admittance Control
Figure: Ott, Christian, Ranjan Mukherjee, and Yoshihiko Nakamura. "Unified impedance and admittance control." Robotics and Automation (ICRA), 2010 IEEE International Conference on. IEEE, 2010.
Notes: Impedance control defines forces as a result of external motions imposed by the environment
Admittance control defines motions as a result of external forces

## Slide 6
Example System Dynamics
  System with θ ∈ RN:
  Nominal trajectory defined by θ0
  Eqn. 1 defines second order system dynamics, low level PD controller
  Eqn. 2 defines forced spring-mass-damper linear dynamics of desired set points
Background: Admittance Control
Desired joint set points
Set Point Second Order Dynamics
Notes: Equation (1) represents the controlled second-order dynamics for the system, where the low-level controller is a standard PD control law.
What makes this an admittance controller is that the desired set point θd in (1) has its own set of dynamics that adjust θd in response to external forcing, measured by τext. Equation (2) specifies that the desired joint signal θd has the linear dynamics of a forced spring-mass-damper, with a nominal trajectory defined by θ0
m is an inertia, kd and kp are positive gains, τext is the torque due to the external force, Md is an effective mass, Bd an effective damping, and Kd an effective spring constant.

## Slide 7
Dynamic Movement Primitive (DMP)
  Generalized form of admittance control
  ƒ is a forcing term, used to modulate response of y
  Freedom in choosing ƒ is what makes this a more general form of admittance control
Background: DMPs
Admittance Control
(Eqn 2)
Dynamic Movement
Primitive
Notes: The freedom in choosing f is what makes DMPs more general than admittance controllers.
An admittance controller can be thought of as a special case of a DMP, where the forcing signal f in (3) is explicitly a function of proprioceptively-measured environmental forces

## Slide 8
Shape Functions
  Composed of two elements:
    (1) Shape bases
    (2) Shape parameters
  Maps a point (σ) in the shape parameter space Σ, into the joint space of a mechanism, i.e., h : Σ → RN, where θ ∈ RN defines the joint space for an N-joint mechanism
Linear Shape Functions
Shape-Based Compliant Control
Shape Parameters
Shape Bases
Notes: βi(s)’s are linearly independent shape basis func- tions. These basis functions spatially encode static joint-to- joint coordination, i.e., these basis functions encode static shapes for a particular mechanism. The expression for h in (5) can be used to map (1) and (2), that define an admittancecontroller in joint space, into an equivalent expression in the shape parameter space Σ using the following relationships
γ = {d, 0}; σd defines a desired shape parameterization and σ0 a nominal shape parameterization. The Jacobian matrixJ in (7) is an analytical Jacobian that arises from changing coordinates from the shape parameter space to the joint space [18].
  Compliant control of shape parameters effectively equivalent to compliant control of joint angles, but the overall shapes a mechanism is allowed to take on are constrained to remain within a particular basis (specified by the βi’s)

## Slide 9
Linear Shape Functions
  Above can be used to map admittance control system equations into equivalent expressions in shape space via relationships:
  Which results in admittance control equation:
Shape-Based Compliant Control
Notes: γ = {d, 0}; σd defines a desired shape parameterization and σ0 a nominal shape parameterization. The Jacobian matrixJ in (7) is an analytical Jacobian that arises from changing coordinates from the shape parameter space to the joint space [18].
Which they then turn into a DMP in shape space by substituting a forcing term
Equivalent to F = J tau_ext
----- Meeting Notes (9/18/16 19:16) -----
DMP not Admittance control

## Slide 10
Hirose’s Serpenoid Model
  Rewrite the above kinematic model into shape function form:
Whole Body Shape-Based Compliance
Notes: Note that in(11), θ, κ, t ∈ RN, where κ and t are actually N ×1 vectors of ones multiplied by the corresponding parameter values, and sin() acts component-wise.
The serpenoid model in (11) is a whole-body kinematic model in the sense that changing any of the parameters κ, A, η, or ω changes the shape of the entire robot.
Because this shapefunction is linear in the elements of σ, a shape-based compliant controller of the form (9) can be derived and implemented on the snake robot hardware

## Slide 11
Amplitude parameter adapting to external forces
Whole Body Shape-Based Compliance

## Slide 12
Defining Spatial Activation Windows
  Shape Function:
Decentralized Shape Modulation
# Activation
Windows
Window Amplitudes
Window Widths
Window Center Locations
Notes: For example, in the lower limit, selecting a single window located at each joint with a small window width effectively decouples shape modulation completely. In the upper limit, a single window located in the center of the mechanism with a large window width represents entirely coupled shape modulation.
additional freedom in (13) is the ability to specify how or if the activation windows move as a function of time. The method chosen in this work is to allow activation windows to move with the waveform sin(ηs − ωt) as it travels down the robot’s body
When each window center travels the distance that brings it to the original position of the window center in front of it, the window is recirculated back to its original position.
Additional constraints pass shape parameters from one window to the next at the times when the window center locations are recirculated.

## Slide 13
Using 3 Windows, Ext. Force Effects on Amplitude Parameters
Decentralized Shape Modulation
W = 3
σ = (A1, A2, A3)
η = 1.5
Notes: ----- Meeting Notes (9/18/16 19:16) -----
omega not W

## Slide 14
Extension to Three Dimensional Motion

## Slide 15
Locomotion Time Results
Notes: “CPG with force” experiment, the CPG model in [7] was modified such that the stabilizing amplitude dynamics in the oscillator equations were augmented to include an “amplitude force” equal to that used in the nine-window shape controller,i.e., Fσ = Jτext−Foffset
The resulting amplitude dynamics for the forced CPG controller were thus equivalent to those used in the shape-based compliant control implementation
The only practical difference between the forced CPG control and the nine window shape-based compliance was that the shape- based controller used traveling spatial windows where the CPG approach had windows fixed at the joint positions.

## Slide 16
Shape Parameters:
  Shape bases: β = [-1, 1]
Hexapod Robot Shape Model

## Slide 17
Hexapod Robot Compliant Locomotion

## Slide 18
Questions?